## Slide 1
Life Under Your Feet
Johns Hopkins University
Computer Science
Earth and Planetary Sciences
Physics and Astronomy
http://www.lifeunderyourfeet.org

## Slide 2: Today
Introduce Life Under Your Feet
Show some data
Our current goals and future directions

## Slide 3: Long-Term Environmental Monitoring

## Slide 4
Notes: Note the small battery
Need to last in the field for ~ 1 year

## Slide 6: Sensor Network Design Philosophies
Use low cost components
No access to line power
  Deployed in remote locations
Radio is the biggest consumer of power
  Minimize radio communication
Transfer data in bulk (amortize radio costs)
  Data Latency vs. Lifetime tradeoff

## Slide 8: All Data Online and available!
http://dracula.cs.jhu.edu/luyf/en/tools/VZTool/
Notes: Data slide

## Slide 9: Deployments

## Slide 10: Cub hill locations (50)

## Slide 11: Soil Temperature Dataset
Notes: - Note the scale. Multiple days worth of data missing and faulty

## Slide 12: Data Features
  Correlated in time and space
  Evolving over time (seasons)
  Diurnal patterns
  Gappy (Due to hardware failures)
  Faulty (Noise, Jumps in values)

## Slide 13: Goals
Leverage spatiotemporal correlations:
Model-based fault detection
Increase network lifetime
  Retrieving data from representative locations
  Use model to interpolate at other locations
  Tradeoff latency for reduced communication

## Slide 14: Examples of Faults

## Slide 15: Motivation for both goals
Environmental Scientists want fault-free data and want to see visualizations
  ~ 5% of data is faulty
Networks need to last a year or more
They start looking at the actual data much much later
  Opportunity to postpone collecting all data

## Slide 16: Soil Temperature Dataset
Notes: - Note the scale. Multiple days worth of data missing and faulty

## Slide 17: Sketch
Estimate fixed common effect (daily median)
Subtract location-specific deviation from this common effect
Model residuals using PCA
  Basis defined in the spatial domain
  Initialized using good data
  Vectors are randomized and fed one by one
    Tamas’ incremental robust PCA
  Gaps corrected using L2 minimization
  Outlier rejection
    Robust function downweights outlier vectors
    Threshold reprojection error to remove outlier measurements

## Slide 18: Initialization
Good
Period

## Slide 19: Tamas’ Iterative and Robust gap-filling (MATLAB)
Notes: 2 purposes
Visualization
Detect faults

## Slide 20: Smooth / Original

## Slide 21: Original and Ratio

## Slide 22: Moving forward
Better way to model these correlations?
  Use some of your methods
How do we use correlations to redesign our data collection subsystem
  2 phase operation
  Periodically download from everyone (infrequent)
  In between, download from representative locations
  Use correlations to interpolate and present to scientists
  Postpone downloading all data in bulk much later
  Extend network lifetime