## Slide 1: Brazil Timestamp Reconstruction

## Slide 2: Problem: Reboots
Too many Reboots!

## Slide 3: Existing Issues
Reboots happen
  unable to trace bug(s) causing them
Current Time reconstruction
  Heavily dependent on the basestation
  BS can go down
  BS can drift even if synced to NTP periodically. Possibly due to network outages
FIX : Need to resort to tricks and magic to reconstruct segments with no anchors and multiple reboots.

## Slide 4: Better Fix : Friends of Friends
Assume one of the nodes knows the global clock (e.g. A dedicated GPS node)
Each nodes beacons the following periodically
<nodeid, rbtCounter, localclock>
Listening nodes record these advertisements and form a local-local anchor pair
<node1, rc1, lc1, node2, rc2, lc2>
  Listen After reboots
  Periodically (once a day/ 12 hrs/ 6hrs depending on reboot rate!)
Eventually someone will know how to get to the globalclock

## Slide 5: Example
GPS
Node
Data
Node
<node1, lc1, rbt1>
<node2, lc2, rbt2>
<node2, lc2, rbt2, globalclock>
<node1, lc1, rbt1, globalclock>

## Slide 6: Example
1
2
3
4
Time
Recovered
Chi (1,2)
Chi (2,4)
Chi (3,4)
Chi (1,3)
Chi (2,3)

## Slide 7: Example

## Slide 8: Example

## Slide 9: Example

## Slide 10: Node States & Events
SENSE
(final)
DOWN
(final)
LISTEN
Sample
beacon
Sleep
Receive
Turning off
Multiple
Reboots
Power up
Periodic
Anchor
collection
Turning off

## Slide 11: Simulation Parameters
  Topology : Cub hill
  Segment Model : Poisson (mu) [ ~ 2 days ]
    Prob (stay down for a while) = 0.05
    Amount of time node stays down ~ U (0 12hrs)
  Beacon frequency (30s)
  Wake up / Listen (after reboot & every “x” hours)
  Communication Model
    Neighbor : Anyone within 30m of another node
    Communication delay ~ U(10ms, 20 ms)
    Prob (success) = 0.95
  Clock Drift : x ppm ( typically, 40 ppm)
  GPSSync : On Reboot & every 6 hours
  Known sensing process : Sine (1 day) + trend
  Sampling Frequency : 30s

## Slide 12: Data
Unixts 
Fake Data value (Sine + trend) 

## Slide 13: Segments
Unixts 
Localclock 

## Slide 14: Implementation
Java 1.5
Used priority queues to simulate time

## Slide 15: Timestamp Reconstruction (C#)
Form a forest of <nodes, rbt#> pairs
Form all <local, local> fits
  record the goodness of fit (ChiSquare)
Create fit for the GPS segments
curr = {gpsSegments}
While (!empty(curr))
  a = Dequeue(curr)
  If exists(globalFit(a) & localFit(a,b)) // for all neighbors of a
    currFit(b) = Map (a,b) // use <a,b> local fit to get a global fit for b
    If ChiSquare(currFit (b) < globalFit(b))
      globalFit (b) = currFit (b) // if new fit is better, update!
      Update ChiSquare (b)
      Parent(b) = a // update new parent of a
    Enqueue(curr, b) // Add b to curr list
End of While

## Slide 16: 1 week simulation - No Drift
54 nodes (1 GPS node + 53 Sensing nodes)
214 segments
Anchors collection scheme
  All neighbors
  6 hour collection
0 s err

## Slide 17: Reconstruction with Clock Drift

## Slide 18: Error CDF

## Slide 19: Explore Further
More sophisticated drift in localclock
Add a random noise to the process (sine + trend + noise)
Optimal # of anchors needed for a given accuracy
Space-accuracy tradeoff
  Collecting anchors from all neighbors is costly (space wise)
    Is it really needed?
  More anchors from a few reliable neighbors with long segments should be better
Earliest reconstruction (online case) Vs Best reconstruction
  Currently Djiktra-like algorithm used for reconstruction
Reboots are not random
  Link reboots to download times