## Slide 1
Temporal Integrity Challenges
in Long-term Environmental
Monitoring Sensor Networks.
Jayant Gupchup†
Alex Szalay±, Andreas Terzis†
Department of Computer Science, Johns Hopkins University†
Department of Physics and Astronomy, Johns Hopkins University±

## Slide 2: Data Collection History

## Slide 3: A Typical Sensor Network
Gateway/
Basestation
Stable
Storage
3.6 V
19.0 Ah
…….
Notes: Bring a box and explain the contents. Leave out optimization stuff. Operate for long periods of line.

## Slide 4: Post Mortem Time Reconstruction
Clock-Synchronization is expensive (power-wise)
  Motes operate asynchronously
  Each mote uses a local clock
Measurements are marked using local clock (LTS)
GTS = α * LTS + β
  GTS is the global timestamp (unixts)
  α is the clock skew
  β is the start time
Periodically collect (LTS,GTS) pairs. “Anchor Points”
Estimate [α β]
Slope (α ):
Clock Skew
β
Notes: Expand Anchor points

## Slide 5: Sources of Errors & Effects
Motes Reboot (data comes in segments)
  Low Battery
  High Moisture
  Software bugs
  Motes stay down for indefinite period
Global clock source can be off
  Sync Global clock source (GPS, Network time protocol)
After every reboot < α , β > needs to be re-estimated

## Slide 6: Bitten by the clock
Lessons Learnt
Synchronize global clock source(s)
Collect more anchor points for reliability and robustness

## Slide 7: Validation and Extreme cases
Reconstruct timestamps if no anchor points are collected
  Global clock source goes down
  Nodes get disconnected from the network

## Slide 8: Annual Solar Patterns
<LOD, noon> = f (Latitude, Time of Year)

## Slide 9: “Sundial”
Length of day (LOD)
Noon
Local Noon | Global Noon
Lts 1 | Gts 1
Lts 2 | Gts 2
… | …
… | …
Lts n | Gts n
“Anchor Points”
argmax lag Xcorr (LOD lts, LOD gts, lag)

## Slide 10: Summary
Postmortem timestamp reconstruction can be non-trivial
Thought needs to go in during system design
Fall back on data-driven reconstruction methods when all else fails.

## Slide 11: Questions
Courtesy : http://upload.wikimedia.org/wikipedia/commons/4/46/Atacama_cosmology_telescope_night.jpg

## Slide 12: Collecting Anchors (<local, global>)
Chart: # Nodes
| Leakin | Olin-I
 | 6 | 10
Chart: # Nodes
| Jugbay-II | Jugbay-I
 | 8 | 13
Chart: # Nodes
| Olin-II | USDA | SERC | Cub hill
 | 19 | 22 | 36 | 53
2009

## Slide 13: Segments
“Leakin” Deployment
MicaZ motes
20 minute sampling
6 boxes
Max Size : 587 days
“Jug bay” Deployment
Telos B motes
30 minute sampling
13 boxes
Max Size : 167 days

## Slide 14: Reconstruction Results
Day Error
Offset in days
Proportional to Error in
Intercept (β)
Minute Error
RMSE Error in minute within the day
Proportional to Error in slope/clock
drift (α)